## Slide 1
Presenter: M. C. Hsu 許銘真
E-mail: exo050282@gmail.com
Phone: 0988946307
The Correction of 3D Reconstructed
Ball Grid Array (BGA) Shape
Notes: 3D 錫球影像的校正

## Slide 2: Outline
The Problem
Iterative Reconstruction
  ART (Algebraic Reconstruction Technique)
  SART (Simultaneous Algebraic Reconstruction Technique)
FBP (Filtered Back Projection)
Notes: Simultaneous Algebraic Reconstruction Technique 同步代數重建法

## Slide 3: The Problem
Reconstruction of 3D solder ball
SOD: Source to Object Distance
SID: Source to Image Distance
Notes: Solder: 焊接
PCB（Printed circuit board）
3D: 3 Dimensions
phi : angle of rotation
Theta : the angle between tube to detector and vertical line.

## Slide 4: The Problem
32 Projections
Notes: 11.25度

## Slide 5: The Problem
Solder balls are too rhombus.
Image contrast not clear enough (voids are dark spots).
VG: Volume Graphics
FBP: Filtered Back Projection
Notes: Rhombus: 菱形
影像對比度不夠清晰（空隙是黑點）。

## Slide 6: Iterative Reconstruction
Notes: Measured projections: 實測投影
Estimated projections: 估測影像
projection-space error 投影空間誤差
image-space error:影像空間誤差

## Slide 7: ART (Algebraic Reconstruction Technique)
A classic iterative reconstruction method.
Additive:

## Slide 8: Additive ART
ART: Algebraic Reconstruction Technique
11
9
7
13
12
8
Notes: Orignal
垂直、對角、水平

## Slide 9: Additive ART
ART: Algebraic Reconstruction Technique
0 | 0
0 | 0
0
0
11
9
Vertical
Notes: 初始0

## Slide 10: Additive ART
ART: Algebraic Reconstruction Technique
5.5 | 4.5
5.5 | 4.5
10
10
12
8
Horizontal
Notes: 初始0

## Slide 11: Additive ART
ART: Algebraic Reconstruction Technique
6.5 | 5.5
4.5 | 3.5
10
10
13
7
Diagonal
Notes: 初始0

## Slide 12: Additive ART
ART: Algebraic Reconstruction Technique
Final
Notes: 初始0

## Slide 13: Additive ART
ART: Algebraic Reconstruction Technique
179°
0°
Sinogram
Original image
Notes: 我們通過生成投影來獲得不同角度的投影值，此影像，每個投影 1°，從 1° 到 179°。我們將每個投影的值放在相應的輸出行上
從左開始: 正方=>右三=>圓=>左三=>長方
Sinogram 正玄圖

## Slide 14: Additive ART
1 Iteration
500 Iterations
100 Iterations
180 Projections
ART: Algebraic Reconstruction Technique

## Slide 15: Additive ART
1 Iteration
500 Iterations
100 Iterations
32 Projections
ART: Algebraic Reconstruction Technique
Notes: 跟 180 比，32比較模糊，因為較少的資訊量

## Slide 16: Multiplicative ART
ART: Algebraic Reconstruction Technique
Notes: Multiplicative: 乘法

## Slide 17: Multiplicative ART
1 | 1
1 | 1
2
2
11
9
Vertical
ART: Algebraic Reconstruction Technique
Notes: 初始=>1
分母=>標準
分子=>目前

## Slide 18: Multiplicative ART
Horizontal
5.5 | 4.5
5.5 | 4.5
10
10
12
8
ART: Algebraic Reconstruction Technique

## Slide 19: Multiplicative ART
6.6 | 5.4
4.4 | 3.6
9.8
10.2
13
7
Diagonal
ART: Algebraic Reconstruction Technique

## Slide 20: Multiplicative ART
Final
ART: Algebraic Reconstruction Technique

## Slide 21: Multiplicative ART
1 Iteration
500 Iterations
100 Iterations
ART: Algebraic Reconstruction Technique
180 Projections

## Slide 22: Multiplicative ART
ART: Algebraic Reconstruction Technique
1 Iteration
500 Iterations
100 Iterations
32 Projections

## Slide 23: Additive vs Multiplicative
Additive ART has better image quality, but more noise is present.
Given less projections, Additive ART gives a more complete picture while Multiplicative ART introduces a lot of previously non-existent entities.
Additive
180 Projections
500 Iterations
Multiplicative
180 Projections
500 Iterations
Additive
32 Projections
500 Iterations
Multiplicative
32 Projections
500 Iterations
ART: Algebraic Reconstruction Technique
Notes: Additive ART 具有更好的圖像質量，影像更完整，但存在更多噪聲。
由於投影較少，Additive ART 提供了更完整的圖片，而 Multiplicative ART 引入了許多以前不存在的實體。

## Slide 24: SART: Simultaneous Algebraic Reconstruction Technique
Considers all projection rays in one iteration
Resist noise
Generate better reconstructed image
Notes: SART同步代數重建法
ART 中每次迭代考慮一根投影射線
SART考慮所有投影射線
抗噪，ART中的噪声进行了平滑，
可以生成更好的重建圖像。
=============================================================================================================
ART 每一次迭代只能修正一條射線上的值；實際上，空間中每個voxel 在一次迭代的運算中，不只一條射線穿過它，所以SART 可以同時修正同一個投影中的所有射線估測值
因此收斂速度上會比ART 快一些

## Slide 25: 3D Reconstruction by SART
SART: Simultaneous Algebraic Reconstruction Technique
DOI: Distance between Object and Image
DSO: Distance between Source and Object
Notes: As for the process of 3D reconstruction, we just conduct a reverse operation. We use image P to interpolate image P’.
After acquiring P’ in different angles, we can use SART to reconstruct the 3D object layer by layer.
至於3D重建的過程，我們只是進行了逆向操作。我們使用圖像 P 來插入圖像 P'。在不同角度獲取P’後，我們可以使用SART逐層重建3D對象。

## Slide 26: 3D Reconstruction by SART (128 Projections)
SART: Simultaneous Algebraic Reconstruction Technique
. . . . . .

## Slide 27: 3D Reconstruction by SART (128 Projections)
SART: Simultaneous Algebraic Reconstruction Technique
Height z = 120
Height z = 100
Height z = 80
Height z = 60
Height z = 40
Height z = 20

## Slide 28: 3D Reconstruction by SART (128 Projections)
Even after increasing contrast, void is visible but unclear
SART: Simultaneous Algebraic Reconstruction Technique
Notes: 把其中一部分放大，且在增加對比的情況下，空隙是可見的但還是不清楚

## Slide 29
FBP: Filtered Back Projection
Back Projection
Filter Back Projection
Star Artifact
Remove the Blur Place
Notes: Back projection reconstructs an image by taking each angle view.
反投影通過獲取每個角度視圖來重建圖像。

## Slide 30
The reconstructed image by FBP.
Projection images with different rotations.
FBP: Filtered Back Projection
FBP

## Slide 31: FBP - Pipeline
FBP: Filtered Back Projection
Input Image
Create Filter
Fourier Transform
Filter
Inverse Fourier Transform
Back Projection
Normalization
Output
Notes: Ramp filter=> 高通濾波
Hann filter
Hamming filter
Cosine filter
Shepp-Logan filter
We use the Hann filter due to higher contrast.

## Slide 32: FBP vs SART
(a) The reconstructed image with height pixels by FBP.
(b) The reconstructed image with height pixels by SART.
(a)
(b)
SART: Simultaneous Algebraic Reconstruction Technique
FBP: Filtered Back Projection

## Slide 33: FBP vs SART
(a) The reconstructed image with height pixels by FBP.
(b) The reconstructed image with height pixels by SART.
(a)
(b)
SART: Simultaneous Algebraic Reconstruction Technique
FBP: Filtered Back Projection

## Slide 34: References
https://en.wikipedia.org/wiki/Solder_ball
https://slideplayer.com/slide/4893938/, 2015.
https://www.slideshare.net/DanielePelliccia/from-filtered-backprojection-to-statistical-tomography-reconstruction, 2018.
https://www.slideshare.net/ZhejianPeng/zjpeng3dsolderballreconstruction, 2017.
https://youtu.be/CwXgFtx6vxs?t=80, 2017.
Hung-Yi Chen, ”3D Reconstruction with X-Ray Images”, 2017.
https://link.springer.com/chapter/10.1007/978-981-10-2772-7_6, 2016.
https://blog.csdn.net/pannn0504/article/details/78357607, 2018.
https://zh.wikipedia.org/wiki/%E5%85%89%E6%B5%81%E6%B3%95
https://www.cnblogs.com/zyly/p/9508131.html, 2018.
https://www.itread01.com/content/1544874242.html, 2018.
https://en.wikipedia.org/wiki/Scale-invariant_feature_transform
https://sci-hub.se/10.1109/nssmic.2012.6551902, 2013.